## Slide 1: TRAINING: REVIEW OF SELECT RADIATION SAFETY PROCEDURES AT UTHealth For Individuals Who Have Met Minimum Radiation Safety Training Requirements at Another Institution
Radiation Safety Program
Environmental Health and Safety
713-500-5840
https://www.uth.edu/safety/radiation-safety

## Slide 2: UTHealth SHERM Mission
Safety, Health, Environment & Risk Management’s (SHERM) mission is to work in conjunction with the UTHealth community to ensure that education, research, and health care service activities take place in conditions that are optimally safe and healthy for all students, faculty, staff, visitors, surrounding community and the general public.
Put simply, we exist to help people go home as healthy and safe as they arrived.

## Slide 3: Radiation Safety Oversight
Radiation Safety Program
  (713) 500-5840
  https://www.uth.edu/safety/radiation-safety/index.htm
Radiation Safety Committee
  https://www.uth.edu/safety/radiation-safety/radiation-safety-committee.htm
Radiation Control, Texas Department of State Health Services
  http://www.dshs.state.tx.us/radiation/default.shtm

## Slide 4: Radiation Safety Training Requirements
Individuals working with radioactive materials (RAM) are required to attend Basic radiation Safety Training at UTHealth
To be considered eligible for exemption from Basic Radiation Safety Training (BRST) at UTHealth:
  1st, provide documentation of radiation safety training at another institution that meets the minimum requirements of BRST at UTHealth
  2nd, complete “TRAINING: REVIEW OF SELECT RAIDATION SAFTEY PROCEDURES AT UTHealth”

## Slide 5: Review of Select Radiation Safety Procedures at UTHealth
Rules, Regulations, Rights, Responsibilities
ALARA and Units
Exposure Limits
Detectors
Laboratory Procedures
Wipe Test
Waste Disposal
Ordering RAM
Spills/Emergencies
Safety Evaluations
More Information (Forms, Manuals, etc)

## Slide 6: Rules, Rights, & Responsibilities of Radiation Workers
Texas Department State of Health Services
  http://www.dshs.state.tx.us/radiation/
In Accordance with Texas Radiation Control Act, Health & Safety Code, Ch 401
25 TAC (Texas Administrative Code) § 289

## Slide 7: Becoming a New Rad PI
Complete the following forms (available on our website):
  RS-01A: Application for Non-Human Use of Radioactive Material OR RS-07: Application for RAM Use in Animals
  RS-01B: Training, Experience, Laboratory Staff and Equipment Form
Usage approved by Radiation Safety Committee
Opening survey of new authorized rad lab
If amendments need to be made use:
  RS-11: Radioactive Material Authorization Amendment Form

## Slide 8: Becoming a New Rad Lab Worker
Complete the following forms (available on our website):
  RS-02: Radiation Safety Training and Experience Form
  RS-03: Dosimetry Service Agreement and Exposure History Form (If needed)

## Slide 9: Keep Doses ALARA
As Low As Reasonably Achievable
How?
  Time
  Distance
  Shielding
Why?
  Minimize Dose

## Slide 10: Time
Less time = Less radiation exposure
Use RAM only when necessary
Shorten time when near RAM
Dry runs (without radioactive material)
  Identify portions of the experiment that can be altered in order to decrease exposure times
Obtaining higher doses in order to get an experiment done quicker is NOT “reasonable”!

## Slide 11: Distance
Effective & Easy
Inverse Square Law
  Doubling distance from source, decreases dose by factor of four
  Tripling it decreases dose nine-fold
More Distance = Less Radiation Exposure
Tongs, Tweezers, Pipettes, Pliers

## Slide 12: Shielding
Materials “absorb” radiation
Proper shielding = Less Radiation Exposure
Plexiglass vs. Lead

## Slide 13: UNITS: Exposure
Charge produced in air from ionization by gammas and x-rays
  ONLY for photons in air
  Rather infrequently used unit
Roentgen (R)
A measure of what is emitted

## Slide 14: UNITS: Absorbed Dose
Energy deposited by any form of ionizing radiation in a unit mass of material
Roentgen Absorbed Dose (rad)
Gray (Gy)
1 Gy = 100 rad
1 rad = 1 cGy = 0.01 Gy

## Slide 15: UNITS: Dose Equivalent
Scale for equating relative hazards of various types of ionization in terms of equivalent risk
Damage in tissue
Q : risk of biological injury
rem = Q * rad
rem (Roentgen Equivalent Man)
Sievert (Sv)
1 Sv = 100 rem

## Slide 16: What Do We Really Need to Know About Units?
1 R  1 rad = 1 rem
    -For gammas & betas
1 rad  1 rem
    -For alphas, neutrons & protons
    -1 rem = 1 rad * Q

## Slide 17: Why Limits?
Non-stochastic Effects (Acute)
  Eliminate Ability to Occur
  Example: Skin Reddening
Stochastic Effects (Chronic)
  Reduce Probability of Occurrence to Same Level as Other Occupations
  Example: Leukemia
ALARA Principal
Established from Accident Data

## Slide 18: Whole Body Dose
Total Effective Dose Equivalent (TEDE)
TEDE = Internal + External
Assume Internal Contribution Zero
    Unless Ingestion, Absorption or Inhalation Suspected
Limit = 5 rem / yr

## Slide 19: Declared Pregnancy
Up to Individual to Declare
  If decides to declare, consult with Radiation Safety and implement procedures
    Involves discussion of the individual’s exposures, work setting and opportunities to minimize radiation level such as with time. Distance and shielding
Legally can’t force someone to declare
  In rare cases, declaration may change job duties
Limits
  Exposure should not exceed 0.05 rem/month
  Exposure shall not exceed 0.5 rem/gestation period

## Slide 20: Annual Exposure Limits
 | rem | mrem
Whole-Body | 5 | 5,000
Eye | 15 | 15,000 May change to 5000 in near future
Shallow | 50 | 50,000
Minors & Declared Pregnant Workers* | 10 % | 10 %
General Public Limit = 2 mrem / hr or 0.1 rem / yr

## Slide 21: Who Needs Dosimetry?
Those “likely” to exceed 10% of their annual limit are required
Those who would like a badge
Minors & Declared Pregnant Workers*

## Slide 22: Comparison of Administrative, Regulatory and Biological Effect Doses
100% of People Die, CNS Syndrome
Permanent Infertility
Whole Body Regulatory Limit (5 rem/yr)
Eye Regulatory Limit (15 rem/yr)
50% of People Die (300 – 500 rad)
Nausea & Vomiting (10% of People)
Whole Body UTHealth Administrative Limit (0.125 rem/month)
Whole Body Exposure
Partial Body Exposure
Extremities Regulatory Limit (50 rem/yr)
Eye UTHealth Administrative Limit (0.375 rem/month)
Rad or Rem
Extremities UTHealth Administrative Limit (1.275 rem/month)
General Public Whole Body Regulatory Limit (0.100 rem/yr)
No Clinical Symptoms Seen Below 10 rem
Cataract Formation
Loss of Hair
Skin Reddening
Decreased White Blood Cell Count
Ulcers on the Skin
Molecular Death (> 100,000 rad)
Gastrointestinal Syndrome

## Slide 23: Radiation Detectors
Portable Laboratory Survey Meter
  Example: GM
  Required unless work with H-3 only
  Annual calibration requirement
Detector for Removable Contamination
  Liquid scintillation counter

## Slide 24: Important Safety Info in Your Lab
Notice To Employees
Emergency Procedures
Waste Disposal Procedures
Radiation Safety Manual
Radiation Safety “Binder”

## Slide 25: Typical Items in Radiation Lab
GM Meter
Radiation Shield
Liquid Scintillation Counter
Caution Radioactive Material Label

## Slide 26: Avoiding Exposure
THERE SHOULD BE NO EATING, DRINKING, SMOKING, APPLYING MAKE-UP OR MOUTH-PIPETTING IN THE LAB!

## Slide 27: Personal Protective Equipment
  Safety Glasses
  Lab Coat
  Disposable Gloves
Inappropriate
Appropriate
  Clothing that Effectively Covers the Legs
  Close-toed Shoes
  Personal Monitoring (in some cases)

## Slide 28: Wipe Test: When and Where?
If you are actively using isotopes
  “Full” wipe test must be documented MONTHLY
If you are merely storing RAM
  Storage location must be wipe tested MONTHLY
If no RAM is used or stored
  Written statement on the wipe test form (no RAM usage or storage in XXX month) should be generated MONTHLY
  Or contact Radiation Safety to go inactive RAM status

## Slide 29: “Full” Wipe Test Procedure
Several wipes should be taken in room where RAM is used
  Use cotton swab to take samples from different areas within the room
  At least one of storage area
Place samples in separate vials or envelopes
Label each vial or envelope noting the location of the sample
Fill out “Laboratory Wipe Test Report” Form (RS-08)
  Form can be found on our website

## Slide 30: Filling out the Report (RS-08)
Fill out all necessary information
  Authorized user
  Date
  Building and Room number
  Wipe tested by
Draw and label laboratory diagram in space provided
Attach LSC results to RS-08

## Slide 31: Collecting the Sample
Take samples in an “S” motion while rotating the cotton swab

## Slide 32: Preparing the Samples
Samples are placed individually in separate vials or eppendorf tubes and LSC cocktail is added
A blank vial/eppendorf tube is prepared in the same manner

## Slide 33: Analyzing the Samples
Place tubes into vial holders
Insert tubes into LSC racks
Load racks into the Liquid Scintillation Counter (LSC) and flag the samples for counting.
Flag:
  Slide the tab located on the rack to the position where the color is showing (This tells the LSC that the sample has not been read).
  When the tab is in the opposite position it tells the user that the sample has been read.

## Slide 34: Analyzing the Samples
Tab position indicates vials not read.
Tab position indicates vials read.

## Slide 35: Reading the Data
Locate the Background CPM in the left column of the Minimum Detectable Activity (MDA) & Action Level Sheet
Find the Action Level that corresponds to the background level
  If the sample has a higher CPM than the action level then the sample area is contaminated

## Slide 36: Quick Contamination Check
If the MDA sheet is not accessible the a rule of thumb for determining if the area is contaminated is if the sample CPM is greater than three (3) times that of the background
Contaminated area > (3)*(Background)

## Slide 37: Survey with GM Counter
Also a good idea to survey work area, lab coat after working with RAM
H-3 not detected by Geiger-Mueller (GM) counter (too low energy beta)
Most other isotopes used in research detected by GM
  Near contact with surface
  Go over surface slowly

## Slide 38: Environmental Protection Program Mission
Ensures the proper disposal of all waste streams: Radioactive, Chemical, and Biological
Monitors releases from the university in the form of air, water, and assets.
Wasteline 713-500-5837
  1 - Radioactive
  2 - Chemical
  3 - Biological

## Slide 39: Prior to Using RAM
Isotopes and concentrations are evaluated during:
  Radiation Safety Committee
  Radiation Safety Program
  Environmental Protection Program
Efforts are made to steer research towards using exempt isotopes and quantities to enhance health and safety and lower waste disposal expenditures

## Slide 40: Storage Principles
Shield appropriately
  Beta emitters - Plexiglas
  Gamma emitters - lead
Survey frequently
Remove when full

## Slide 41
Solid
Liquid
LS Vials
Biological
Mixed
Waste Streams at UTHealth

## Slide 42: Solid Waste
Waste is segregated at the point of generation
Segregation Scheme:
  < 300 day half life (32P, 35S)
  > 300 day half life (3H, 14C)
Placed in black opaque bags inside of properly labeled 5 gallon container
Close bag and fasten with tape or tie wrap
Securely attach completed waste tag
Deposit in the appropriate drum in alcove

## Slide 44: Liquid Waste
Waste is segregated at the point of generation
Segregation Scheme
  keep all isotopes separate
Bulk liquid waste in 1 gallon pre-labeled containers provided
  Place first two washes into container
Complete attached waste tag
Call the Wasteline
Liquid waste should be a neutral aqueous based solution (chemical based requires approval)

## Slide 45: Liquid Scintillation Vials
Waste is segregated at the point of generation
Segregation Scheme
  < 300 day half life (32P, 35S)
  > 300 day half life (3H, 14C)
Placed in black opaque bags inside of properly labeled 5 gallon container
Close bag and fasten with tape or tie wrap
Securely attach completed waste tag
Deposit in the appropriate drum in regional alcove

## Slide 46: Liquid Scintillation Cocktails
Liquid scintillation cocktail should be “biodegradable”
Flash point > 140 deg. F.

## Slide 47: Biological/Radioactive Waste
Segregation Scheme
  keep all isotopes separate
Place carcass in black opaque bag (separate associated waste and place in solid waste)
Put adsorbent into bag (available from EPP)
Attach completed label to bag (identify if the waste is infectious)
Place in freezer in basement or call Wasteline
Approval required for work with animals

## Slide 48: Mixed Waste
Mixed waste is regulated by the EPA under RCRA and by Radiation Control, TX DSHS
Make sure the bottle is labeled or the original label is intact and legible
Call the Wasteline for disposal
  713-500-5837

## Slide 49: Hazardous Waste Alcove Locations
Refer to:
  https://www.uth.edu/safety/radiation-safety/radioactive-waste-alcove-locations.htm
  Green “Important Safety Information” posting in your lab

## Slide 50: Ordering Radioactive Material
Only authorized individuals can order radioactive materials
EACH order of radioactive material MUST receive pre-approval by Radiation Safety
All radioactive material MUST be delivered to Radiation Safety

## Slide 52: Correct Units
“Rad Mat” approvals must be submitted in “millicuries” (mCi). Amounts in microcuries (μCi) must be converted: 1mCi = 1000 μCi.
Examples:
500 μCi = 0.5 mCi
250 μCi = 0.25 mCi
10 μCi = 0.01 mCi

## Slide 53: Carrier Delivery Location of ALL Radioactive Materials
Radiation Safety, UTHealth
  Attn: Primary Investigator
  6431 Fannin CYF G. 102
  Houston, TX 77030
Researchers pick-up packages from Radiation Safety office unless outside Medical School Complex
Friendly reminder to carrier
  Radiation Safety must receive all radioactive packages
Bring package, packing list and primary vial to radiation safety

## Slide 54: Inventory Form
Track inventory use on “inventory form”
Vial Disposal Record

## Slide 55: Source Security
No radioactive material in corridors!
Radioactive waste is not to be in hallways
Transportation of radioactive sources through hallways is allowed
  Minimize potential for contamination by using secondary containment

## Slide 56: Spills and Radiation Emergencies
Minor Spill:
  Contain spill
  Clean up spill or contact Radiation Safety for help if you do not feel comfortable cleaning up the spill by yourself
Major Spill
  Contain spill
  Contact Radiation Safety immediately

## Slide 57: Cleaning a RAM Spill
Ensure that spill is contained
  Limit traffic where event occurred.
  Prevent runoff (from table to floor or spreading on table)
  Inform coworkers and lab manager.
  Call Radiation Safety
Obtain necessary supplies for cleanup
  Paper towels or diapers
  RADCON or Scrubbing Bubbles (DOW)
  Opaque plastic bags for waste.
  Labels
  Gloves
  Descriptive forms (RS4 form)

## Slide 58: How to Clean Up a Spill
Spray area with RADCON or Scrubbing Bubbles (DOW)
Wipe from the outside in so not to spread the contamination
After removable contamination has been removed and fixed contamination has been covered & labeled,
  Retake and document GM meter readings
  Detail preventive actions with coworkers
  Complete Incident Report

## Slide 59: Safety Evaluations
Comprehensive radiation inspections twice a year by EH&S
Annual inspection focus includes chemical and biological hazards
Follow-up of deficiencies not corrected on-site

## Slide 60: Sample Questions
Radiation Safety
Physical Safety
General Safety
Fire Safety
Chemical Safety

## Slide 61: For More Information
Basic Radiation Safety Training Manual
Training Guidebook: Review of Select Radiation Safety Procedures at UTHealth
Radiation Safety Manual
All Manuals Available at: https://www.uth.edu/safety/radiation-safety/radiation-safety-manual.htm

## Slide 62: Useful Forms
RS-01A - Application for Non-Human Use of Radioactive Material
RS-01B - Training, Experience, Laboratory Staff, and Equipment
RS-07 - Application for Radioactive Material Use in Animals
RS-08 - Laboratory Wipe Test Report for RAM for Authorized Users
RADMAT - Radiation Materials Request Form
All Forms Available at:
https://www.uth.edu/safety/radiation-safety/index.htm

## Slide 63: Additional Available Radiation Safety Training
6-hr Basic Radiation Safety Training
    Required for Radioactive Material Users
X-Ray Producing Devices
Bone Densitometry Safety
Laser Safety
  Class IIIb and IV Lasers

## Slide 64
Radiation Safety Program
Environmental Health & Safety
713-500-5840